## Slide 1: CUSTOMER ORDER SCHEDULING WITH LOT STREAMING TO MINIMIZE THE TOTAL ORDER COMPLETION TIME IN A TWO-MACHINE FLOW SHOP
Günce YOZGAT
M.Sc. Thesis Defense Seminar
February 5, 2018
Çankaya University, Department of Industrial Engineering
Thesis Supervisor: Assoc. Prof. Dr. Ferda Can ÇETİNKAYA

## Slide 2: Outline
Problem Definition and Complexity
Literature Review
Mixed Integer Linear Programming (MILP) Model
Proposed Heuristic Algorithm
Computational Experiments
Conclusions and Future Research Directions

## Slide 3: 1. Problem Definition and Complexity 1.1. Definition
M1
M2
There are K customer orders and N products (jobs) in two machine flow shop environment.
Each customer order can request a variety of products (jobs).
All products are first processed by machine 1 and then machine 2.

## Slide 4: 1. Problem Definition and Complexity 1.2. Assumptions
Overlapping of the two operations on the same product through the creation of sublots (i.e., lot streaming) is allowed without intermingling the sublots of other products.
Preemption of the sublots is not allowed; i.e., any sublot cannot be interrupted until the completion of its operation.
No setup is necessary between successive sublots of the same product.
All customer orders are available for processing at the same time, say time 0.
Each machine is available at time zero and remains continuously available.
Each machine can process at most one sublot at a time and each sublot can be processed on only one machine at any given time.
Sufficient storage space exists to stock the processed sublots on machine 1.
Transportation times between machines are considered to negligible.

## Slide 5: 1. Problem Definition and Complexity 1.3. Complexity
Customer order scheduling problem with lot streaming to minimize the total completion time in a two-machine flow shop is NP-hard in the strong sense.
Finding a sequence of the jobs and the sequences of the sublots in each job to minimize total order completion time at the same time.

## Slide 6: 1. Problem Definition and Complexity 1.4. Contribution of the Thesis
The contribution of this thesis is threefold.
To the best of our knowledge, there is no study that considers the flow shops with both customer order scheduling (COS) and lot streaming (LS).
We formulate the problem as a mixed integer linear programming (MILP) model to solve the problem optimally.
Our proposed heuristic algorithm is straightforward and easy to implement for finding optimal and near-optimal solutions for medium and large-sized problem instances.

## Slide 7: 2. Literature Review 2.1. Customer Order Scheduling (COS) Problems
Single Machine | Parallel Machines | Open Shop and Job Shop
Gupta et al. (1997) Makespan | Yang and Postner (2005) Total completion time of batches | Wagneur and Sriskandarajah (1993) Total completion time
Gerodimos et al. (2000) Number of late jobs | Yang (2005) Makespan, maximum lateness completion time | Liu (2010) Customer order flow time
Erdal and Ghosh (2007) Total order completion time | Leung et al (2005) Maximum lateness | 
Hazir et al. (2008) Average Customer flow time | Lin and Kononov (2007) Number of late jobs | 
 | Wang and Chend (2007) Weighted order completion time | 
 | Xu et al (2015) Total completion time | 

## Slide 8: 2. Literature Review 2.1. Multi-job Lot Streaming (LS) Problems
Paper | Makespan
Vickson and Alfredsson (1992) | ✔
Vickson (1995) | ✔
Kalir (1999) | ✔
Kalir and Sarin (2001) | ✔
Defersha and Chen (2010) | ✔
Glass and Possani (2011) | ✔
Mortezaei and Zulkifli (2013) | ✔
Çetinkaya (1994) | ✔
Çetinkaya and Kayagil (1992) | ✔
Çetinkaya and Duman (2010) | ✔
Liu (2009) | ✔

## Slide 9: 3. Mixed Integer Linear Programming (MILP) Model 3.1. Sets and Indices

## Slide 10: 3. Mixed Integer Linear Programming (MILP) Model 3.2. Parameters

## Slide 11: 3. Mixed Integer Linear Programming (MILP) Model 3.3. Decision Variables

## Slide 12: 3. Mixed Integer Linear Programming (MILP) Model 3.4. Model

## Slide 13: 3. Mixed Integer Linear Programming (MILP) Model 3.4. Model

## Slide 14: 3. Mixed Integer Linear Programming (MILP) Model 3.4. Model

## Slide 15
Proposed Heuristic Algorithm
Number of products (jobs)
Number of orders (sublots)
Reasonable Computational Time
Low Success Level for Real Life Problems
3. Mixed Integer Linear Programming (MILP) Model
3.5. Computational Effort

## Slide 16: 4. Proposed Heuristic Algorithm
Termination Condition?
Reading Data
Phase 1
Finding an Initial Job Sequence
Phase 2
Improving the Initial Job Sequence by the Insertion Algorithm
Phase 3
Improving the Initial Job Sequence by Pairwise Interchanging
Phase 4
Finding a Better Solution
by the Tabu-search Algoritm
Proposed Heuristic Algorithm Solution
NO
YES

## Slide 17
4. Proposed Heuristic Algorithm
4.1. Numerical Example
We have 5 orders and 5 products (jobs).
Notes: Sayıyla 5 order 5 jobımız var diye not koyacaksın

## Slide 18
Phase 1: Finding an Initial Job Sequence
Step 1:
4. Proposed Heuristic Algorithm
4.1. Numerical Example
Notes: Orderları aynı hizaya al, renklendir, orderların hepsi aynı anda gelecek

## Slide 19
M1
M2
Orders | CT( )
 | 390
 | 461
 | 543
 | 423
 | 483
minimum
Phase 1: Finding an Initial Job Sequence
Step 2:
4. Proposed Heuristic Algorithm
4.1. Numerical Example

## Slide 20
M1
M2
RI2= 83
Products | RIj
 | 83
 | 54
 | 80
Update the Order List
Initial job sequence
Updated Order List
4. Proposed Heuristic Algorithm
4.1. Numerical Example
Phase 1: Finding an Initial Job Sequence
Step 3: Run-in time calculation
minimum
Step 2
Notes: Run in ve oku en son gelecek, j5 i seçmeyi de göster

## Slide 21
M1
M2
Orders | CT( )
 | 250
 | 309
 | 391
 | 307
 | 340
minimum
Phase 1: Finding an Initial Job Sequence
Step 2:
4. Proposed Heuristic Algorithm
4.1. Numerical Example

## Slide 22
M1
M2
RI5= 80
Products | RIj
 | 83
 | 80
Update the Order List
Initial job sequence
Updated Order List
4. Proposed Heuristic Algorithm
4.1. Numerical Example
Phase 1: Finding an Initial Job Sequence
Step 3: Run-in time calculation
minimum
CT =4799

## Slide 23
Phase 2: Improving the Initial Job Sequence by the Insertion Algorithm
J4 - J5 - J2 - J3 - J1
CT =1602
CT =1968
J4 – J5
J5 – J4
J2 – J4 – J5
J4 – J2 – J5
J5 – J4 – J2
CT =3237
CT =3362
CT =3400
J3 – J2 – J4 – J5
CT =3947
J2 – J3 – J4 – J5
CT =4097
J2 – J3 – J4 – J5
CT =4194
J2 – J3 – J4 – J5
CT =4194
J1 – J3 – J2 – J4 – J5
J3 – J1 – J2 – J4 – J5
J3 – J2 – J1 – J4 – J5
J3 – J2 – J4 – J1 – J5
J3 – J2 – J4 – J1 – J5
CT=5072
CT=4922
CT=4862
CT=4670
CT=4605
4. Proposed Heuristic Algorithm
4.1. Numerical Example
CT =4799

## Slide 24
Phase 3: Improving the Job Sequence Obtained in Phase 2 by Pairwise Interchanging the Sublots of the Jobs
CT =4632
with CT =4605
4. Proposed Heuristic Algorithm
4.1. Numerical Example
Notes: Hepsinin puntolarını düzelt

## Slide 25
Phase 4: Finding a Better Solution by the Tabu-Search Algorithm
-
Phase 3
4. Proposed Heuristic Algorithm
4.1. Numerical Example
Phase 3
Phase 3
Phase 3

## Slide 26
-
-
--
-
-
--
-
-
-
-
Phase 4: Finding a Better Solution by the Tabu-Search Algorithm
-
--
4. Proposed Heuristic Algorithm
4.1. Numerical Example
Phase 3
Phase 3
Phase 3

## Slide 27
M1
M2
4. Proposed Heuristic Algorithm
4.1. Numerical Example

## Slide 28: 5. Computational Experiments 5.1. Computer Software Packages
To evaluate the effectiveness and efficiency;
MILP Model
Solved by GAMS 24.1 under the time limit of 3 hour with the computer having Intel (R) Xeon (R) CPU E52650 0@ 2.00GHz 2.00 GHz (2 Processors) and 128 GB RAM.
Proposed Heuristic Algorithm
Coded in Java programming language on a personal computer with Intel Core i7 Dual-Core 2.00 GHz CPU and 8 GB RAM.

## Slide 29: 5. Computational Experiments 5.2. Computational Settings for Test Problem
Number of customer orders (K): 5 and 10
Number of products (jobs) (N): 5, 10, 15 and 20
, and : DU[1, 10] and DU[1,K].
: DU[0, 100f], where f is taken as
0.0, 0.5, 1.0, 1.5, and 2.0.
200 problem instances are generated for setup case.
200 problem instances are generated for no setup case.

## Slide 30: 5. Computational Experiments 5.3. Performance Measures
: Percent deviation from the optimal solution
: Percent deviation from the best integer solution
:

## Slide 31: 5. Computational Experiments 5.4. Discussion of Results 5.4.1. Setup Case
Performance of the MILP
Number of customer orders (K) | 5 |  |  |  | 10 |  |  | 
Number of jobs (N) | 5 | 10 | 15 | 20 | 5 | 10 | 15 | 20
Total number of problem instances considered | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25
Number of optimum integer solutions obtained in 3 hours | 25 | 1 | 0 | 0 | 4 | 0 | 0 | 0
Number of best integer solutions obtained | 0 | 24 | 25 | 25 | 21 | 25 | 25 | 25
Average gap (%) | 0 | 45 | 78 | 87 | 38 | 85 | 91 | 93
Total Average gap (%) | 64.7 |  |  |  |  |  |  | 

## Slide 32: 5. Computational Experiments 5.4. Discussion of Results 5.4.1. Setup Case
Average Percent Deviations of the Heuristic Algorithm from the Optimal and Best Integer Solution
N | K | Number of Problem Instances Give Optimal Solution | Average Percent Deviation of Heuristic Algorithm from Optimal Solution |  | Number of Problem Instances Give Best Integer Solution |  | Average Percent Deviation of Heuristic Algorithm from Best Integer Solution | AVG. | MAX. DEV.
5 | 5 | 25 | 0.36% |  | - |  | - | 0.36% | 2.59%
 | 10 | 4 | 0.00% |  | 21 |  | 1.51% | 1.27% | 7.66%
Grand Avg_5 |  | 0.81% |  |  |  |  |  |  | 
10 | 5 | 1 | 0.61% | 24 |  | 1.11% |  | 1.09% | 9.34%
 | 10 | - | - | 25 |  | 0.82% |  | 0.82% | 4.54%
Grand Avg_10 |  | 0.96 % |  |  |  |  |  |  | 
15 | 5 10 | - | - | 25 |  | 0.52% |  | 0.52% | 3.52%
 | 10 | - | - | 25 |  | 0.44% |  | 0.44% | 7.11%
Grand Avg_15 |  | 0.48% |  |  |  |  |  |  | 
20 | 5 | - | - | 25 |  | 0.08% |  | 0.08% | 1.62%
 | 10 | - | - | 25 |  | 0.00% |  | 0.00% | 0.00%
Grand Avg_20 |  | 0.04% |  |  |  |  |  |  | 
AVG_TOTAL |  | 0.57% |  |  |  |  |  |  | 

## Slide 33: 5. Computational Experiments 5.4. Discussion of Results 5.4.2. No Setup Case
Performance of the MILP
Number of customer orders (K) | 5 |  |  |  | 10 |  |  | 
Number of jobs (N) | 5 | 10 | 15 | 20 | 5 | 10 | 15 | 20
Total number of problem instances considered | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25
Number of optimum integer solutions obtained in 3 hours | 25 | 2 | 0 | 0 | 4 | 0 | 0 | 0
Number of best integer solutions obtained | 0 | 23 | 25 | 25 | 21 | 25 | 25 | 25
Average GAP (%) | 0 | 42 | 80 | 89 | 38 | 90 | 94 | 96
Total Average GAP (%) | 66.4 |  |  |  |  |  |  | 

## Slide 34: 5. Computational Experiments 5.4. Discussion of Results 5.4.2. No Setup Case
Average Percent Deviations of the Heuristic Algorithm from the Optimal and Best Integer Solution
N | K | Number of Problem Instances Give Optimal Solution | Average Percent Deviation of Heuristic Algorithm from Optimal Solution | Number of Problem Instances Give Best Integer Solution | Average Percent Deviation of Heuristic Algorithm from Best Integer Solution | AVG. | MAX. DEV.
5 | 5 | 25 | 2.26% | - | - | 2.26% | 12.64%
 | 10 | 4 | 0.00% | 21 | 1.14% | 0.96% | 7.93%
Grand Avg_5 |  | 1.61% |  |  |  |  | 
10 | 5 | 2 | 8.52% | 23 | 2.52% | 3.00% | 14.73%
 | 10 | - | - | 25 | 1.00% | 1.00% | 3.98%
Grand Avg_10 |  | 2.00 % |  |  |  |  | 
15 | 5 10 | - | - | 25 | 1.55% | 1.55% | 8.26%
 | 10 | - | - | 25 | 0.50% | 0.50% | 3.71%
Grand Avg_15 |  | 1.03% |  |  |  |  | 
20 | 5 | - | - | 25 | 0.18% | 0.18% | 1.76%
 | 10 | - | - | 25 | 0.46% | 0.46% | 6.57%
Grand Avg_20 |  | 0.32% |  |  |  |  | 
AVG_TOTAL |  | 1.24% |  |  |  |  | 

## Slide 35: 5. Computational Experiments 5.4. Discussion of Results 5.4.3. Setup Case vs No Setup Case
Comparison of the Setup and No Setup Cases for MILP Performance for orders
five
ten
Case | Setup Case |  |  |  | No Setup Case |  |  | 
Number of customer orders is 5 (K=5) | 5 |  |  |  | 5 |  |  | 
Number of jobs (N) | 5 | 10 | 15 | 20 | 5 | 10 | 15 | 20
Total number of problem instances | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25
Number of optimum integer solutions | 25 | 1 | 0 | 0 | 25 | 2 | 0 | 0
Number of best integer solutions | 0 | 24 | 25 | 25 | 0 | 23 | 25 | 25
Average GAP (%) | 0 | 45 | 78 | 87 | 0 | 42 | 80 | 89
Total Average GAP (%) | 52.7 |  |  |  | 53.2 |  |  | 
Case | Setup Case |  |  |  | No Setup Case |  |  | 
Number of customer orders is 10 (K=10) | 10 |  |  |  | 10 |  |  | 
Number of jobs (N) | 5 | 10 | 15 | 20 | 5 | 10 | 15 | 20
Total number of problem instances | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25
Number of optimum integer solutions | 4 | 0 | 0 | 0 | 4 | 0 | 0 | 0
Number of best integer solutions | 21 | 25 | 25 | 25 | 21 | 25 | 25 | 25
Average GAP (%) | 38 | 85 | 91 | 93 | 38 | 90 | 94 | 96
Total Average GAP (%) | 77 |  |  |  | 80 |  |  | 

## Slide 36: 5. Computational Experiments 5.4. Discussion of Results 5.4.3. Setup Case vs No Setup Case
Average Percent Deviations
N | K | Number of Problem Instances | Average Percent Deviation for Setup Case | Max. Deviation for Setup Case | Average Percent Deviation for No Setup Case | Max. Deviation for No Setup Case
5 | 5 | 25 | 0.36% | 2.59% | 2.26% | 12.64%
 | 10 | 25 | 1.27% | 7.66% | 0.96% | 7.93%
Grand Avg / Total |  | 50 | 0.81% | 5.12% | 1.61% | 10.28%
10 | 5 | 25 | 1.09% | 9.34% | 3.00% | 14.73%
 | 10 | 25 | 0.82% | 4.54% | 1.00% | 3.98%
Grand Avg / Total |  | 50 | 0.96% | 6.94% | 2.00% | 9.35%
15 | 5 10 | 25 | 0.52% | 3.52% | 1.55% | 8.26%
 | 10 | 25 | 0.44% | 7.11% | 0.50% | 3.71%
Grand Avg / Total |  | 50 | 0.48% | 5.31% | 1.03% | 5.98%
20 | 5 | 25 | 0.08% | 1.62% | 0.18% | 1.76%
 | 10 | 25 | 0.00% | 0.00% | 0.46% | 6.57%
Grand Avg / Total |  | 50 | 0.04% | 0.81% | 0.32% | 4.16%
Total Avg /Total |  | 200 | 0.57% | 4.55% | 1.24% | 7.45%

## Slide 37: 6. Conclusions and Future Research Directions 6.1. Conclusions
MILP model
Proposed Heuristic Algorithm
Setup Case
Promising results for small-and medium-sized problem instances optimally in very short time (less than 45 seconds).
No Setup Case
Near-optimal solutions for large-sized instances in very short computational times(less than 45 seconds).
 | Total Average Deviation | Number of Optimal Solution | Number of Problem Instances Have Better Solution Than MILP Solution Under Time Limit | Number of Problem Instances Having Deviation <1.00% | Number of Problem Instances Having Deviation >1.00%
Setup Case | 0.57% | 47 | 87 | 27 | 39
No Setup Case | 1.24 % | 27 | 73 | 41 | 59
Notes: Detaya gir yüzde ver time da vurgu yap

## Slide 38: 6. Conclusion and Future Research Directions 6.2. Future Research Directions
Allowing intermingling the sublots of different products (jobs).
Manufacturing environment
Flow shops (more than two machine)
Job shops
Open shops
Study of other measures of performance such as
Makespan
Total or maximum lateness
Total tardiness
Number of tardy customer orders
Notes: Tezdeki sırayla anlat

## Slide 39: THANKS FOR LISTENING AND QUESTIONS